## Slide 1
Energy Storage Computational Tool (ESCT) Overview
Developed under DOE Contract DE-FE0004001 Task 430.05
September 2012

## Slide 2
Energy Storage Computational Tool » Overview Summary
The Energy Storage Computational Tool (ESCT) identifies and monetizes the costs and benefits of energy storage (ES) systems deployed in utility applications.
Characteristics of the ESCT |  | Advantages
Primary Purpose | The ESCT is primarily designed to identify, quantify, and monetize the costs and benefits of an operational ES project. So, many of the inputs represent measured data. | Straightforward to use Lends itself to quality control Provides a consistent and credible method for identification and calculation of benefits Ensures consistency of results across projects Well suited for long term analysis
Secondary Purpose | The ESCT can also help the user evaluate the potential costs and benefits of a proposed or hypothetical project. It could also help to optimize the size, type, and location of the ES system. | 
Perspective | The ESCT is designed to account for all benefits including those that accrue to the asset owner, ratepayer/consumer, and societal stakeholders. | 
Data Inputs | Measured data is used where available and estimated data is used for additional benefits that are difficult to measure or quantify. | 
Platform | The ESCT is entirely self-contained in Microsoft Excel and can be saved, edited, and updated. | 

## Slide 3
Project Details
The tool identifies potential benefits and estimates the monetized value for an ES project based on the project details and application specified by the user.
Energy Storage Computational Tool » Conceptual Framework
Example:
Regulatory Structure
Application(s)
Benefits
Is the asset in a regulated market?
How will the asset be used?
Why is that good?
Monetary Value
What is that worth?
Location
Where is the asset located?
Technology
Owner
What ES technology will be used?
Who will own the ES device?
Frequency Regulation
Ancillary Service Revenue
$1.5 MM/year

## Slide 4
Project Details |  | 
Category | Options | Definition
Location | Generation | This location describes any point between the generator and the transmission lines.
 | Transmission | This location describes any point between the beginning of the transmission lines and the step-down distribution substation.
 | Distribution | This location describes any place starting downstream of the power transformer at a step-down distribution substation, until the customer meter.
 | End-User | This location describes any place on the customer-side of the customer meter.
Regulatory Structure | Regulated | A market in which utilities are vertically integrated, incorporating most elements of electric delivery and service into a single company.
 | Deregulated | A market in which vertical integration at utilities has been broken up, allowing for independent power producers and merchant generators.
Owner | Utility | An asset owner that maintains and operates a local transmission and or distribution grid, such as an investor-owned utility, municipal utility, or electricity cooperative.
 | Non-Utility Merchant/IPP | An asset owner that can independently deploy generation and ES assets for wholesale market participation or contracts with utilities or end users.
 | End-User | An asset owner that is primarily an end-user of electricity.
Achievable benefits may vary depending on the location of the ES on the grid, the regulatory structure, the owner, and the type of technology selected.
Energy Storage Computational Tool » Project Context Inputs

## Slide 5
Reference Document – Energy Storage for the Electricity Grid: Benefits and Market Potential Assessment Guide
(SAND2010-0815, February 2010)
http://www.smartgrid.gov/sites/default/files/resources/energy_storage.pdf
The ESCT uses the energy storage applications defined in an energy storage benefits report published by Sandia National Labs in 2010.
ENERGY STORAGE APPLICATIONS
Electric Energy Time Shift
Electric Supply Capacity
Load Following
Area Regulation
Electric Supply Reserve Capacity
Voltage Support
Transmission Support
Transmission Congestion Relief
T&D Upgrade Deferral
Time-of-Use Energy Cost Management
Demand Charge Management
Electric Service Reliability
Electric Service Power Quality
Renewables Energy Time Shift
Renewables Capacity Firming
Wind Generation Grid Integration – Short Duration
Wind Generation Grid Integration – Long Duration
Energy Storage Computational Tool » Storage Applications

## Slide 6
The framework for monetizing benefits applied in the ESCT is consistently used throughout the ARRA-funded DOE Smart Grid programs.
Benefit Category | Benefit Sub-category | Benefit
Economic | Market Revenue | Arbitrage Revenue Capacity Market Revenue Ancillary Services Revenue
 | Improved Asset Utilization | Optimized Generator Operation Deferred Generation Capacity Investments Reduced Congestion Cost
 | T&D Capital Savings | Deferred Transmission Investments Deferred Distribution Investments
 | Energy Efficiency | Reduced Electricity Losses
 | Electricity Cost Savings | Reduced Electricity Cost
Reliability | Power Interruptions | Reduced Outages
 | Power Quality | Improved Power Quality
Environmental | Air Emissions | Reduced CO2 Emissions Reduced SOX, Reduced NOX Reduced PM-2.5 Emissions
Energy Storage Computational Tool » Benefits Framework

## Slide 7
Applications | Economic |  |  |  |  |  |  |  |  |  | Reliability |  | Env. | 
 | Market Revenue |  |  | Asset Utilization |  |  |  |  | Efficiency | Cost | Interruptions |  | Air | 
 | Arbitrage Revenue | Capacity Revenue | Ancillary Service Revenue | Optimized Generator Operation | Reduced Congestion Cost | Deferred Generation Capacity Investments | Deferred Transmission Capacity Investments | Deferred Distribution Capacity Investments | Reduced Electricity Losses | Reduced Electricity Cost | Reduced Outages | Improved Power Quality | Reduced CO2 Emissions | Reduced SOX, NOX, and Particulate Emissions
Electric Energy Time Shift | X |  |  | X |  | X | X | X | X | X |  |  | X | X
Electric Supply Capacity |  | X |  |  |  | X |  |  |  |  |  |  |  | 
Load Following |  |  | X | X |  | X |  |  |  |  |  |  | X | X
Area Regulation |  |  | X | X |  | X |  |  |  |  |  |  | X | X
Electric Supply Reserve Capacity |  |  | X | X |  | X |  |  |  |  |  |  | X | X
Voltage Support |  |  | X |  |  |  |  |  |  |  |  | X |  | 
Transmission Support |  |  |  |  |  |  | X |  |  |  | X |  |  | 
Transmission Congestion Support |  |  |  |  | X |  | X |  |  |  |  |  |  | 
T&D Upgrade Deferral |  |  |  | X |  | X | X | X | X |  |  |  | X | X
Time of Use Energy Cost Management |  |  |  | X |  | X | X | X | X | X |  |  | X | X
Demand Charge Management |  |  |  | X |  | X | X | X | X | X |  |  | X | X
Electric Service Reliability |  |  |  |  |  |  |  |  |  |  | X |  |  | 
Electric Service Power Quality |  |  |  |  |  |  |  |  |  |  |  | X |  | 
Renewables Energy Time Shift | X |  |  | X |  | X | X | X | X | X |  |  | X | X
Renewables Capacity Firming |  | X |  |  |  | X |  |  |  |  |  |  | X | X
Wind Generation – Short |  | X |  |  |  | X |  |  |  |  |  |  | X | X
Wind Generation – Long | X |  |  | X |  | X | X | X | X | X |  |  | X | X
Energy Storage Computational Tool » Applications x Benefits Matrix
The ESCT identifies different benefits depending on the applications pursued.

## Slide 8
Project Details
The tool identifies potential benefits and estimates the monetized value for an ES project based on the project details and application specified by the user.
Energy Storage Computational Tool » Conceptual Framework
Regulatory Structure
Application(s)
Benefits
Is the asset in a regulated market?
Monetary Value
Location
Where is the asset located?
Technology
Owner
What ES technology will be used?
Who will own the ES device?
$1.5 MM/year
Metrics
Calculations
Forecast
What data should be collected?
What equations will calculate value?
How can value be projected into the future?

## Slide 9
The ESCT is composed of three modules that characterize the project, collect data, and calculate the net present value.
Asset Characterization Module
Data Input Module
Computational Module
Purpose | Determine the list of project benefits. | Filter irrelevant metrics. Guide and assist data entry. | Calculation and Present results.
Inputs | Project Details, Applications | List of Benefits | Calculation Dataset, Sensitivity Ranges
Outputs | List of Benefits | Calculation Dataset | Tabular and Graphic Presentation of Monetized Benefits
Key Methodologies | Application-to-Benefit Relational Models | Benefit-to-Input Relational Model | ES Benefit Calculations, Benefit Forecast Methodology
1
2
3
Energy Storage Computational Tool » How the ESCT works

## Slide 10
The ESCT User Guide includes detailed explanations of the methodology as well as step-by-step use instructions.
The first half of the User Guide is dedicated to:
  Providing context for the tool and explaining its purpose;
  Explaining the general methodology for assessing the benefits of an energy storage project; and
  Defining each Application and Benefit.
The second half of the User Guide is dedicated to:
  Explaining the general Architecture of the ESCT; and
  Providing a step-by-step instruction manual for using the ESCT.
The Appendix of the User Guide documents and explains:
  The detailed cost and benefit calculations used in the tool; and
  Key concepts and assumptions (ex. inputs, default values, escalation techniques).
Energy Storage Computational Tool » ESCT User Guide

## Slide 11
The ESCT in Excel, an overview presentation, and the user guide are available for download on SmartGrid.gov.
Energy Storage Computational Tool: http://www.smartgrid.gov/recovery_act/program_impacts/energy_storage_computational_tool
ESCT Overview Presentation: http://www.smartgrid.gov/document/doe_energy_storage_computational_tool_overview
ESCT User Guide: http://www.smartgrid.gov/document/doe_energy_storage_computational_tool_user_guide_12
Energy Storage Computational Tool » ESCT Download Locations

## Slide 12
Key Contacts
    Steven Bossart
US Department of Energy
National Energy Technology Laboratory
3610 Collins Ferry Road
PO Box 880
Morgantown, WV 26507-0880
304-285-4643
steven.bossart@netl.doe.gov
    Colette Lamontagne
    Director
    Navigant Consulting, Inc.
    Burlington, Massachusetts
    781-270-8340
    Colette.Lamontagne@navigant.com
    Warren Wang
    Associate Director
    Navigant Consulting, Inc.
    Pittsburgh, Pennsylvania
    213-618-9019
    WWang@navigant.com
    David Feliciano
    Senior Consultant
    Navigant Consulting, Inc.
    Burlington, Massachusetts
    781-270-8315
    David.Feliciano@navigant.com